 Improved Estimates of Key Seismic Properties of the Crust
Ben Postlethwaite
UBC

---
Overview
- Motivation
- Background Science

---
Motivation: The Problem
Extracting material properties from seismic data has a long history.
For bulk crustal composition under receivers the seismic velocity ratio
has been used.
This provides Poisson's ratio:
which is useful for constraining crustal composition.
Further use of seismic data to constrain crustal composition would require knowledge of explicit values of Vp or Vs.
R = {V_p} over {V_s}
%sigma= {1} over {2} {({V_p} over {V_s} )^2 - 2} over {({V_p} over {V_s} )^2 - 1}
Poisson's Ratio: It is the ratio of lengthening along one axis versus compression along the other two.

---
- Many previous studies have used a grid search for the seismic velocity ratio R = Vp/Vs and crustal thickness H. Kanamori (2000)
- Some a priori information is required, namely an estimate P-wave velocity Vp.
- Here we attempt to recover Vp and seismic velocity ratio R, without any assumption on Vp.
- For accurate resolution of Vp in solution we require sharp deconvolution (close to spike train as possible).
- We try damped-L2 based deconvolution as well as sparsity promoting wavelet-based L1 minimization.

---
Select P-coda as source approx
Deconvolve
Non-linear Fit for Tps
Grid search for Vp, Vs
Line search for H
Curvelet denoise

---
Select P-coda as source approx
Deconvolve
Non-linear Fit for Tps
Grid search for Vp, Vs
Line search for H
Curvelet denoise

---
Motivation - The Problem
- Currently using a Simultaneous Deconvolution with Generalized Cross Validation regularization.
- where F is the Fourier transform matrix, G is the model, S is the S-wave seismogram , P is the P-wave source coda, * is the complex conjugate and δ is the regularization. δ is chosen by minimizing the Generalized Cross Validation function:
Misfit: more accurate with δ -> 0. Less stable.
As δ increases denominator increases, promotes stability.

---
Motivation - The Problem
Confidence of final results highly dependent on sharpness of deconvolution.

---
Sparsity promoting L1 Deconvolution.
- Take advantage of the fact that an optimal receiver function has sparse wavelet representation.
- Design a deconvolution algorithm that leverages sparsity.
- See if it can beat the tried and true L2 deconvolution.